## Slide 1: What’s Next - 802.11ax / WiFi 6
Greg Kamer – Principal Systems Engineer

## Slide 2: 802.11ax – Key Motivations
Protocol Overhead & Inefficiency
Limited Number of Channels
Proliferation of Wi-Fi Devices
  8 Devices/User [2012] to
  50 Devices/User [2022]
  IoT: multiple devices, low bandwidth
Demand for increased Capacity with QoS
  Users’ Apps demand more
    Social Media, On-Demand Video, etc.
Proliferation of battery operated devices
Lot more contention than users estimate
  Single Tx Channel
High Density Environments
  802.11 needs to evolve to work well in dense environments
  Transportation Hubs, Large Public Venues (stadiums)
Increased Outdoor Operation
  Smart City Initiatives, increased connectivity all over the world
Mobile Data Offload - SMS, Twitter, etc.
  ‘Short Packet’ problem
Address 802.11 Limitations
New Use-Cases

## Slide 3: Wi-Fi Evolution
 | 802.11 (Legacy) | 802.11b (Legacy) | 802.11a (Legacy) | 802.11g (Legacy) | 802.11n (HT) | 802.11ac (VHT) | 802.11ax (HE)
Year Ratified | 1997 | 1999 | 1999 | 2003 | 2009 | 2014 | 2019 (Expected)
Operating Band | 2.4 GHz/IR | 2.4 GHz | 5 GHz | 2.4 GHz | 2.4/5 GHz | 5 GHz | 2.4/5 GHz
Channel BW | 20 MHz | 20 MHz | 20 MHz | 20 MHz | 20/40 MHz | 20/40/80/160 MHz | 20/40/80/160 MHz
Peak PHY Rate | 2 Mbps | 11 Mbps | 54 Mbps | 54 Mbps | 600 Mbps | 6.8 Gbps | 9.6 Gbps
Link Spectral Efficiency | 0.1 bps/Hz | 0.55 bps/Hz | 2.7 bps/Hz | 2.7 bps/Hz | 15 bps/Hz | 42.5 bps/Hz | 62.5 bps/Hz
Max # SU Streams | 1 | 1 | 1 | 1 | 4 | 8 | 8
Max # MU Streams | NA | NA | NA | NA | NA | 4 (DL only) | 8 (UL & DL)
Modulation | DSSS, FHSS | DSSS, CCK | OFDM | OFDM | OFDM | OFDM | OFDM, OFDMA
Max Constellation / Code Rate | DQPSK | CCK | 64-QAM, 3/4 | 64-QAM, 3/4 | 64-QAM, 5/6 | 256-QAM, 5/6 | 1024-QAM, 5/6
Max # OFDM tones | NA | NA | 64 | 64 | 128 | 512 | 2048
Subcarrier Spacing | NA | NA | 312.5 kHz | 312.5 kHz | 312.5 kHz | 312.5 kHz | 78.125 kHz
“We need to know where we are coming from to appreciate where we are going”

## Slide 4: Key 802.11ax Enhancements
OFDMA
PHY and MAC Efficiency
Uplink
MU-MIMO
1024-QAM
Power Efficiencies
BSS Coloring
Frequency /Subcarriers

## Slide 5: OFDM vs. OFDMA
Borrowing from modern LTE terminology, the 802.11ax standard calls the smallest sub-channel a Resource Unit (RU)
AP decides how to allocate the channel, always assigning all available RUs on the downlink.
Users will have a smaller, but dedicated, sub-channel, thus improving the average throughput per user

## Slide 6: 802.11ax – OFDMA Enables Spectral Efficiency
Frequency /Subcarriers
Frequency /Subcarriers
Time
Time
User1
User2
User3
User4
OFDM
OFDMA
Full Channel Bandwidth allocated to single user
Overhead doesn’t scale with payload size
Channel BW allocated among multiple users
Overhead amortized across multiple users
Increase in spectral efficiency, Reduced Latency
Supports heterogeneous users – i.e. IM vs Large downloads

## Slide 7: Uplink MU-MIMO
Only Downlink MU-MIMO from AP to STA(s) in 802.11ac
  AP co-ordinated MU grouping of STA(s) and opportunistically transmitted frames
802.11ax introduces Uplink MU-MIMO from STA(s) to
  AP now co-ordinates multiple STA(s) transmitting simultaneously to AP
MU-RTS
to STA(s)
Simultaneous
CTS to AP
Trigger
to STA(s)
Frames to AP
from STA(s)
Multi-STA
Block Ack
AP
STA(s)

## Slide 8: 802.11ax – Multi-User Benefits, OFDMA & MU-MIMO
OFDMA | MU-MIMO
Useful when multiple users have small amount of data | Useful when multiple users have full buffer traffic
Number of concurrent clients can be as high as 74 | Number of concurrent clients limited to 8 (introduced in .11ax)
Effective at all ranges (close, mid, and far) | Effective at close- to mid-range, not effective at far range
No sounding overhead for either DL or UL OFDMA | Sounding required for DL MU, but not for UL MU
Lower latency | Tends to increase latency
Can be used to mitigate OBSS interference issues | No interference mitigation
Complementary techniques to serve multiple users concurrently

## Slide 9: 802.11ax – MAC/PHY Enhancements
 | 802.11ac | 802.11ax
BANDS | 5 GHz | 2.4 GHz and 5 GHz
CHANNEL BANDWIDTH | 20 MHz, 40 MHz, 80 MHz, 80+80 MHz & 160 MHz | 20 MHz, 40 MHz, 80 MHz, 80+80 MHz & 160 MHz
FFT SIZES | 64, 128, 256, 512 | 256, 512, 1024, 2048
SUBCARRIER SPACING | 312.5 kHz | 78.125 kHz
OFDM SYMBOL DURATION | 3.2 us + 0.8/0.4 us CP | 12.8 us + 0.8/1.6/3.2 us CP
HIGHEST MODULATION | 256-QAM | 1024-QAM
PHY RATES | 433 Mbps (80 MHz, 1 SS) 6933 Mbps (160 MHz, 8 SS) | 600 Mbps (80 MHz, 1 SS) 9600 Mbps (160 MHz, 8 SS)
1024-QAM – Higher modulation
Quantum jump in highest achievable PHY rates
11ax benefits extended to 2.4GHz band
Unlike 11ac, Clients in 2.4GHz band benefit as well
Reduced Overhead, Helps Outdoor Operation
Spectral efficiency – more tones/channel

## Slide 10: 802.11ax – More Efficiency with Sub-Carrier Spacing
In 802.11ax, sub-carrier spacing is reduced to enable a 4X increase in the number of available data-tones, compared to earlier 802.11 specifications.
A 4X increase in available data tones, along with 1024-QAM, dramatically increases the maximum PHY rates.
More data tones also enable supporting multiple users (max of 74) with OFDMA

## Slide 11: 802.11ax – Long OFDM Symbol
GI
(Multipath Immunity)
“Useful” Portion of OFDM Symbol
GI
(Multipath Immunity)
“Useful” Portion of OFDM Symbol
GI
(Multipath Immunity)
“Useful” Portion of OFDM Symbol
GI
(Multipath Immunity)
“Useful” Portion of OFDM Symbol
3.2 us
OFDM Symbols in 11g/n/ac
“Useful” Portion of OFDM Symbol
GI
(Multipath Immunity)
12.8 us
GI
(Multipath Immunity)
“Useful” Portion of OFDM Symbol
OFDM Symbols in 11ax (Indoor – Increased Throughput Due to Reduced GI Overhead)
OFDM Symbols in 11ax (Outdoor – Increased Multipath Resilience Due to Longer GI)
12.8 us

## Slide 12: 802.11ax – MAC/PHY Efficiency
 | 802.11a/g | 802.11n/ac | 802.11ax
# of Tones –20MHz | 64 | 64 | 256
Sub-carrier spacing | 20MHz/64 = 312.5KHz | 20MHz/64 = 312.5KHz | 20MHz/256 = 78.125KHz
Data Sub-carriers | 48 | 52 | 234
Efficiency | 75% | 81% | 91%
OFDM Symbol | 3.2us | 3.2us | 12.8us
Guard Interval | 0.8us | 0.4, 0.8us | 0.8, 1.6, 3.2us
Symbol Time | 4.0us | 3.6, 4.0us | 13.6, 14.4, 16.0us
Efficiency | 80% | 90%, 80% | 94%, 89%, 80%
Increasing
PHY-level
Efficiency
~17% more efficient than 11n/ac
~40% more efficient than 11a/g

## Slide 13: 802.11ax – 1024-QAM Constellation
25%
DATA RATE
INCREASE
256-QAM
1024-QAM
constellation diagrams
11ac
11ax

## Slide 14: 802.11ax – Power Efficiency
11ax AP
STA1
STA2
BEACON
TRIGGER
TRIGGER
AP
AWAKE
STA1
STA2
AWAKE
SLEEP
SLEEP
SLEEP
Pre-negotiated Wake times between AP and Clients
Avoids contention on the air among client devices
Scheduled sleep & power-on (awake) times enables efficient power consumptions for clients
TARGET WAIT TIME

## Slide 15: 802.11ax – BSS Coloring
OBSS – OVERLAPPING Basic Service Set
BSS Coloring – Fixes OBSS problem
AP1
User 1
User 2
AP2
User A
AP1
User 1
User 2
AP2
User A
User2 senses interference from both
AP1 & AP2 - User2 cannot transmit till medium is completely clear of both APs
With BSS Coloring, User2 can ignore
Interference from AP2 and transmit as soon as it senses medium is clear of AP1

## Slide 16: 802.11ax Deployment Considerations
5 GHz Band # Radio Chains | 2.4 GHz Band # Radio Chains | Average TCP T’put* | Ethernet Backhaul | Input Power over PoE
8x8 | 4x4 | 2.7 Gbps | 5 Gbps | > PoE+
4x4 | 4x4 | 1.4 Gbps | 2.5 Gbps | PoE+
2x2 | 2x2 | 0.7 Gbps | 1 Gbps | PoE
Multi-Gigabit Peak Wi-Fi PHY Rates call for Multi-Gig Ethernet Backhaul
  Peak TCP rates are ~85% of peak Wi-Fi PHY Rates
  Practical Wi-Fi Spectrum Management considerations dictate useful PHY Bandwidth = 80MHz
Higher Power consumption calls for PoE+ supplies from switch/controller
  Increased power consumption to support higher PHY Rates in 802.11ax