## Slide 1: Aerohive Networks
David Coleman
The Nuts and Bolts of 802.11ax

## Slide 2
Who is this guy?
David Coleman
Senior Technical Evangelist
CWNE #4
@mistermultipath

## Slide 3
Sybex CWNA Study Guide – 5th Edition
ISBN: 978-1119425786
Amazon: http://bit.ly/CWNAv5

## Slide 4
FOUNDED
2006
1st
802.11ax
AP
1st
ENTERPRISE PLUGGABLE AP
1st
PRIVATE
PRE-SHARED
KEY
PIONEERED
CLOUD
NETWORKING
NYSE
HIVE
GLOBAL
CLOUD
FOOTPRINT
PATENTS
60+
500+
EMPLOYEES
30K+
HAPPY
CUSTOMERS
ONLY
PUBLIC, PRIVATE
& PORTABLE
CLOUD

## Slide 5
8802.11ax

## Slide 6
802.11n and 802.11ac technology introduced new PHY and MAC layer enhancements to achieve high data rates
We built bigger highways and faster cars
802.11n and 802.11ac

## Slide 7
But this is the problem:

## Slide 8: The solution:

## Slide 9: Airtime consumption
RF is a half-duplex medium
At any given time only one radio can transmit on a frequency domain (channel)
Everybody takes turns

## Slide 10
Data rate is not TCP throughput
Medium contention protocol of CSMA/CA consumes much of the available bandwidth
Aggregate TCP throughput in a legacy a/b/g environment is 40% – 50% of data rate in ideal conditions
Aggregate TCP throughput in an 802.11n/ac environment is 60% – 70% of data rate in ideal conditions
Data Rates versus Throughput

## Slide 11
High density of clients
Efficiency at the MAC sublayer always drops as more clients stations join
Increase in collisions and medium contention overhead
Traffic nightmare

## Slide 12
The bulk of of data frames (75 -80%) are small and under 256 bytes
The result is overhead at the MAC layer and medium contention overhead for each small frame
Traffic nightmare

## Slide 13
The future: 802.11ax
802.11ax – High Efficiency(HE)
802.11ax uses PHY and MAC layer enhancements for better traffic management
The goal is to increase average throughput 4X per user in high-density scenarios
Operates in both the 2.4 GHz and 5 GHz frequency bands

## Slide 14
OFDMA – better use of the frequency space
BSS Color/Spatial Reuse – Mitigate OBSS
Uplink and Downlink MU-MIMO for up to 8 devices!
1024-QAM – Higher data rates
Target Wake Time (TWT) – Great for IoT devices
The future: 802.11ax- What is new?

## Slide 15
The term multi-user (MU) simply means that transmissions between an AP and multiple clients can occur at the same time dependent on the supported technology.
However, the MU terminology can be very confusing when discussing 802.11ax. MU capabilities exist for both MU-OFDMA and MU-MIMO. Please understand the differences as explained further in this field note.
What is the definition of Multi-User (MU) ???

## Slide 16
OFDMA is the secret sauce!
Notes: OFDMA is combination of frequency domain and time domain multiple access

## Slide 17
OFDM subcarriers (20 MHz)
20 MHz Channel
56 subcarriers (4 pilot and 52 data)
64 subcarriers (312.5 kHz)
Pilot
Data
Null
OFDM divides bandwidth into subcarriers
Data subcarriers – Carry modulated data
Management Subcarriers – Don’t carry data, they are used for synch and interference protection purposes

## Slide 18: OFDM – 802.11a/g/n/ac
Subcarriers
Time
Channel width
Client 1
Client 2
Client 3
Client 4
Client 5
Client 6

## Slide 19
OFDMA
Orthogonal Frequency-Division Multiple Access (OFDMA)
Multi-user version of the popular orthogonal frequency-division multiplexing (OFDM) digital modulation scheme
Multiple access is achieved in OFDMA by assigning subsets of subcarriers to individual clients
This allows simultaneous low data rate transmission to/from multiple users.

## Slide 20: OFDMA – 802.11ax
Subcarriers
Time
Channel width
Client 1
Client 2
Client 3
Client 4
Client 5
Client 6
Resource Unit (RU)

## Slide 21
Frequency allocations for both uplink and downlink OFMDA define resource units (RU) with 26, 52, 106, 242, 484 or 996 subcarriers (tones)
The subcarriers (tones) are in fixed locations of each 20, 40 or 80 MHz channel
OFDMA Resource Units
26
26
26
26
13
13
26
26
26
26
26
52
52
52
52
106
106
242
20 MHz

## Slide 22
OFDMA Resource Units
26
26
26
26
13
13
26
26
26
26
26
52
52
52
52
106
106
242
20 MHz
1 user
2 users
4 users
9 users
Based on multi-user traffic needs, the AP decides how to allocate the channel

## Slide 23
OFDMA Resource Units
26
26
26
26
13
13
26
26
26
26
26
52
52
52
52
106
106
242
20 MHz
1 user
2 users
4 users
9 users
AP may allocate the whole channel to only one user at a time or it may partition it to serve multiple users simultaneously

## Slide 24
Spectrum analyzer view of OFDMA Resource Units

## Slide 25
The rules of medium contention still apply.
The AP still has to compete against legacy 802.11 stations for a transmission opportunity (TXOP).
Once the AP has a TXOP, the AP is then in control of up to nine 802.11ax client stations for either downlink or uplink transmissions.
The number of RUs used can vary on a per TXOP basis.
OFDMA – The AP is in charge!
STA 1
STA 2
STA 3
STA 4

## Slide 26: Downlink MU-OFDMA
AP
STA 4 RU 4 : 52 tones
STA 3 RU 3 : 52 tones
STA 2 RU 2 : 52 tones
STA 1 RU 1 : 52 tones
AIFS
802.11ax AP
SIFS
802.11ax clients
STA 1
CTS
SIFS
BAR
SIFS
Block ACK
SIFS
STA 2
CTS
Block ACK
STA 3
CTS
Block ACK
MU-RTS
Trigger
Multi-user DL-PPDU
STA 4
CTS
Block ACK

## Slide 27: Downlink MU-OFDMA
AP
802.11ax AP
802.11ax clients
STA 1
STA 2
STA 3
MU-RTS
Trigger
STA4
CTS
CTS
CTS
CTS
STA 4 RU 4 : 52 tones
STA 3 RU 3 : 52 tones
STA 2 RU 2 : 52 tones
STA 1 RU 1 : 52 tones
Multi-user DL-PPDU
Block ACK
Block ACK
Block ACK
Block ACK

## Slide 28
AP
AIFS
802.11ax AP
SIFS
802.11ax clients
STA 1
BSR
STA 2
BSR
STA 3
BSR
MU-RTS
STA 4
BSR
BSRP
SIFS
SIFS
CTS
CTS
CTS
CTS
Trigger #1
SIFS
v
Trigger
UL-PPDU
SIFS
UL-PPDU
UL-PPDU
UL-PPDU
Multi-STA Block ACK
SIFS
PAD
Trigger #2
Trigger #3
Uplink MU-OFDMA
Notes: UL-OFDMA is more complex than DL-OFDMA and may require the use of as many as three trigger frames. Each trigger frame is used to solicit a specific type of response from the Wi-Fi 6 clients. UL-OFDMA also requires the use of buffer status report (BSR) frames from the clients. Clients use BSR frames to inform the AP about the client’s buffered data and about the QoS category of data. The information contained in BSR frames assists the AP in allocating RUs for synchronized uplink transmissions. The AP will use the information gathered from the clients to build uplink window times, client RU allocation, and client power settings for each RU. Buffer status reports (BSRs) can be unsolicited or solicited. If solicited, the AP will poll the clients for BSRs.

## Slide 29
AP
802.11ax AP
802.11ax clients
STA 1
STA 2
STA 3
STA 4
BSRP
Trigger #1
Uplink MU-OFDMA
BSR
BSR
BSR
BSR
MU-RTS
Trigger #2
CTS
CTS
CTS
CTS
Trigger
Trigger #3
UL-PPDU
UL-PPDU
UL-PPDU
UL-PPDU
Multi-STA Block ACK
Notes: For UL-OFDMA, a trigger frame sent by the AP is also used to tell the clients how many spatial streams and which modulation and coding scheme (MCS) to use when transmitting uplink on their assigned RUs. This information can be found in the SS Allocation and UL MCS subfields of the user information field within the body of a trigger frame.
Trigger frames can also be used by an AP to tell clients to adjust their power settings for synchronized uplink transmissions. Within a trigger frame, the UL Target RSSI subfield indicates, in a dBm value, the expected receive power at the AP across all antennas for the assigned resource unit (RU) transmissions from the uplink 802.11ax clients. The UL Target RSSI subfield uses values of 0 to 90 which are directly mapped from –110 dBm to –20 dBm. A value of 127 indicates to the client station to transmit at its maximum power for the assigned MCS. Based on this information provided by the trigger frame, the transmit power could be adjusted by the uplink clients. Please note that a client station might be unable to satisfy the target RSSI due to its hardware or regulatory limitations.

## Slide 30
30
Subcarriers
Time
Client 1
Client 2
Client 3
Client 4
Client 5
Client 6
AP sends ‘Trigger’ to alert clients when to transmit
Uplink MU-OFDMA
Notes: AP Still Controls the Medium
Process Overview
  AP sends a Trigger Frame - Buffer Status Report Request (BSRR)
  Clients reply synchronized Buffer Status Report (BSR) frames
    Information about their AID, data length, Type of Date (QoS)
  AP builds RU schedule with following information
    Start, Stop times / Client RU Mapping / RUs per clients / MCS setting/ Power Levels per RU /
  AP sends MU-RTS
  CTS responses from the clients in parallel (RU)
  AP sends Trigger to allocate the RUs and time-sync
  Clients send UL-DATA via their assigned RUs
  Multi-User Block ACK from the AP

## Slide 31: Buffer Status Reports
APs require specifics on client buffer states to perform appropriate RU scheduling, two approaches available:
Clients deliver Buffer Status Reports (BSRs) to assist the AP in allocating UL MU resources.
  Clients can explicitly deliver BSRs to the AP in response to a BSRP trigger frame (solicited BSR).
  Clients can implicitly deliver BSRs in the QoS Control field or BSR Control field of any frame transmitted to the AP (unsolicited BSR)
In either case AP will determine client transmit requirements
Notes: Additionally, the buffer status report poll (BSRP) trigger frame is not needed when the Wi-Fi 6 clients send unsolicited buffer status report information. Clients can send unsolicited BSRs in frames using either of these subfields:
QoS Control field: Wi-Fi 6 client station can report buffer status information for any given QoS class of traffic in the Queue Size subfield of the QoS Control field in QoS Data or QoS Null frames it transmits. Additionally, an 802.11ax client can report the buffer status of multiple QoS access categories using A-MPDU frame aggregation of QoS Data or QoS Null frames. Traffic identifiers (TIDs) are used to indicate the QoS access category of the buffered client traffic. The Queue Size subfield indicates the amount of buffered traffic for any given traffic class.
BSR Control field: See the next slide

## Slide 32: Unsolicited buffer status reports and A-MPDU
Wi-Fi 6 client station can report unsolicited buffer status information for any given QoS class of traffic in any QoS Data or QoS Null frames it transmits.
Additionally, an 802.11ax client can report the buffer status of multiple QoS access categories using A-MPDU frame aggregation of QoS Data or QoS Null frames.
PHY header
MSDU-1
MAC
header
MPDU-1
Trailer
MSDU-2
MAC
header
Trailer
MSDU-3
MAC
header
Trailer
MPDU-2
MPDU-3
BlockACK
MAC
header
PHY
header
I need to send some buffered voice and video traffic!
BSR - Voice
BSR - Voice
BSR - Video

## Slide 33
26 tone RU | RU-1 | RU-2 | RU-3 | RU-4 | RU-5 | RU-6 | RU-7 | RU-8 | RU-9
Subcarrier range | -121:-96 | -95:-70 | -68:-43 | -42:-17 | -16:-4, 4:16 | 17:42 | 43:68 | 70:95 | 96:121
RU allocation bits | 0000000 | 0000001 | 0000010 | 0000011 | 0000100 | 0000101 | 0000110 | 0000111 | 0001000
52 tone RU | RU-1 |  | RU-2 |  |  | RU-3 |  | RU-4 | 
Subcarrier range | -121:-70 |  | -68:-17 |  |  | 17:68 |  | 70:121 | 
RU allocation bits | 0100101 |  | 0100110 |  |  | 0100111 |  | 0101000 | 
106 tone RU | RU-1 |  |  |  |  | RU-2 |  |  | 
Subcarrier range | -122:-17 |  |  |  |  | 17:122 |  |  | 
RU allocation bits | 0110101 |  |  |  |  | 0110110 |  |  | 
242 tone RU | RU-1 |  |  |  |  |  |  |  | 
Subcarrier range | -122:-2, 2:122 |  |  |  |  |  |  |  | 
RU allocation bits | 0111101 |  |  |  |  |  |  |  | 
RU Allocation
Notes: As previously mentioned, trigger frames contain information about RU allocation. RU allocation information is communicated to clients at both the PHY and MAC layers. RU allocation information can be found in the HE-SIG-B field of the PHY header of an 802.11 trigger frame.
Additionally RU allocation information is delivered in the user information field in the body of a trigger frame. This slide displays a table of how RU allocation information is communicated at the MAC layer.
The table highlights all the possible RUs within a 20 MHz channel and the subcarrier range for each RU. Each specific RU is defined by a unique combination of 7 bits within the user information field of the trigger frame.

## Slide 34
802.11ax AP
802.11ax clients
STA 1
STA 2
STA 3
Trigger
Trigger
STA 1: 52 tone – RU-1 | 
Subcarriers: -121:-70 | 
Bit index: 0100101 | 
STA 2: 52 tone – RU-2
Subcarriers: -68:-17
Bit index: 0100110
STA 3: 106 tone - RU-2
Subcarriers: 17:122
Bit index: 0110110
SIFS
Multi-STA Block ACK
SIFS
RU Allocation
Notes: In the example, the trigger frame allocates specific RUs to three client stations for simultaneous uplink transmission within a 20 MHZ ODMA channel. Client STA-1 and STA-2 are each assigned to a 52-tone RU while client STA-3 is assigned to a 106-tone RU.

## Slide 35
The client can suspend and resume Uplink Multiuser operation and/or Downlink Multiuser operation.
OMI initiator
OMI responder
I want to contend for the medium all by myself, and go single user!
Fine…. Be that way!
Operating mode indication (OMI)

## Slide 36: MU-MIMO

## Slide 37: MU-MIMO
AP use DL MU-MIMO to serve multiple clients requires spatially diverse position.
AP can specify multiple STA to simultaneously send uplink frames via trigger frames.
AP
User1
User2

## Slide 38
MU-MIMO….. not so much
Less than 5% of the currently available clients support MU-MIMO
  Hardly any MU-MIMO capable clients exist in the current marketplace and the technology is rarely used in the enterprise

## Slide 39
MU-MIMO
Even if all clients supported MU-MIMO, the majority of modern-day enterprise deployments of Wi-Fi involve a high density of users that is not conducive for MU-MIMO conditions
  MU-MIMO requires spatial diversity, therefore physical distance between the clients is necessary
20 feet
25 feet
15feet
20 feet
30 feet

## Slide 40
MU-MIMO
The majority of modern-day indoor enterprise deployments of Wi-Fi involve a high density of users that is not conducive for MU-MIMO conditions

## Slide 41
Downlink MU-MIMO was introduced with Wave-2 802.11ac access points, however, real-world implementation of MU-MIMO has still not occurred and currently is not practical:
  MU-MIMO requires transmit beamforming (TXBF) which requires sounding frames. The sounding frames add excessive overhead, especially when the bulk of data frames are small
  MU-MIMO would only be a favorable option in very low client density, high bandwidth environments
  Support for uplink MU-MIMO will not be in 1st generation chipsets
Which is better… MU-OFDMA or MU-MIMO?

## Slide 42: BSS Color

## Slide 43
Does RF just stop?
Almost impossible to prevent CCI at 2.4 GHz
Co-Channel Interference (CCI)
Channel 1
Channel 1
Channel 6
Channel 11

## Slide 44
CCI is not static and always changing
Client transmissions cause CCI
Co-Channel Interference (CCI)
Channel 1
Channel 1
Channel 6
Channel 11

## Slide 45
The BSS color is a numerical identifier (color) of the BSS
802.11ax radios are able to differentiate between BSSs using BSS color identifier when other radios transmit on the same channel
BSS Color

## Slide 46
intra-BSS
inter-BSS
+ 4 dB
-76 dBm
CCA – energy detect threshold
CCA – Adaptive signal detect threshold
Noise Floor
-96 dBm
-100 dBm
-83 dBm
BSS Color – Spatial Reuse
Adaptive CCA implementation could raise Signal Detect threshold for inter-BSS frames, while maintaining a lower threshold for intra-BSS traffic

## Slide 47
Additional 802.11ax capabilities

## Slide 48
Target Wake Time (TWT) is a power saving mechanism in 802.11ah, negotiated between a STA and its AP, which allows the STA to sleep for periods of time, and wake up in pre-scheduled (target) times to exchange information with its AP
This allows the station to ‘sleep’ longer and reducing energy consumption.
Key feature for IoT type sensors
Target Wake Time

## Slide 49
Devices can sleep for longer periods
Saves battery life
Ideal for IoT devices
Target Wake Time

## Slide 50
Much like 256-QAM, we anticipate that very high SNR thresholds (~ 35 dB) will be needed in order for 802.11ax radios to use 1024-QAM modulation.
1024-QAM modulation
Notes: Although the goal of 802.1ax is better efficiency as opposed to higher data rates, there is one exception. First generation 802.11ax radios will support 1024-QAM modulation which will also mean some new modulation and code schemes (MCS) that define some higher data rates. 256-QAM modulates 8 bits per symbol whereas 1024-QAM modulates 10 bits per symbol, meaning there is potential 20 percent increase in throughput.
As a result, 802.11ax introduces two new modulation and coding schemes, MSC-10 and MSC-11 which will most likely be optional. 1024-QAM can only be used with 242-tone resource units or larger. This means that at least a full 20 MHz channel will be needed for 1024-QAM.

## Slide 51
802.11ax Key Questions

## Slide 52
802.11ax
Wi-Fi Alliance
Wi-Fi Alliance has introduced a new generational Wi-Fi naming system that helps users better understand the experience they can expect
Wi-Fi 6 is the next generation of Wi-Fi based on 802.11ax technology: www.wi-fi.org/wi-fi-6
802.11ac
802.11n

## Slide 53
The answer is yes and no!
802.11ax APs will not improve the performance or range of any legacy Wi-Fi clients (802.11a/b/g/n/ac)
802.11ax clients will be needed to take full advantage of 802.11ax high efficiency capabilities such as multi-user OFDMA
Is there any benefit for legacy clients?

## Slide 54
The answer is yes and no!
However, as we see more 802.11ax clients mixed into the client population, the efficiency improvements gained by 802.11ax client devices will free valuable airtime for those older clients, therefore improving the overall efficiency of the system.
There will be also be enhanced performance as a result of newer hardware capabilities of the new 802.11ax APs, such as stronger CPUs, better memory handling, etc.
Is there any benefit for legacy clients?

## Slide 55
Where are the 802.11ax clients?
The Elephant in the room!

## Slide 56
Where are the 802.11ax clients?
We all know that there are no 802.11ax clients yet
They are coming!
  Broadcom 2x2:2
  Qualcomm 2x2:2
  Intel 2x2:2
The Elephant in the room!
Notes: 1 billion Wi-Fi 6 chipsets will ship annually by 2022
Source: ABI Research

## Slide 57
Wi-Fi 6 clients coming soon!
Vendors announcing 802.11ax end-user devices:
HP OMEN Asus ROG Mothership
Samsung Galaxy S10 & S10+
ABI Research: 1 billion Wi-Fi 6 chipsets will ship annually by 2022

## Slide 58
Some of our competitors are claiming we will need 10 Gbps uplinks from 802.11ax APs. Is this true?
NO!
Bandwidth bottlenecks are almost always the WAN uplink
What about uplink connections?

## Slide 59
Will we at least need 2.5 MultiGig (802.3bz) Ethernet ports?
As 802.11ax client populations grow, 2.5 MultiGig may be needed
Will we need MultiGig switch ports?

## Slide 60
Aerohive’s Dual 5-GHz radio capability makes this even more likely!
The AP650 and AP650X will each have a 2.5G and 1G (full duplex) Ethernet uplink port.
Will we need MultiGig switch ports?

## Slide 61
The extra radio chains and quad-core processor will require more power
802.3at PoE Plus power of 25 watts will be required
PoE Plus requirements for 4x4:4 MIMO APs should be considered a standard requirement
Will 802.11ax APs work with 802.3af PoE?

## Slide 62
Some vendors will have 8x8:8 APs
Power of 31 watts per port and much higher will be a requirement for 8x8:8 APs
Or two PoE Plus cable runs
Will 802.11ax APs work with 802.3af PoE?

## Slide 63
Some of our competitors may manufacture an 8x8:8 access point using a Qualcomm IPQ8074 chipset. It will support eight 5 GHz streams and four 2.4 GHz streams. Some key points should be understood about 8x8:8 APs versus 4x4:4 802.11ax APs:
8x8:8 APs will initially be more expensive and require more power
8x8:8 APs do not offer more client connectivity per AP
Which is better? 8x8:8 or 4x4:4 APs?

## Slide 64
8x8:8 APs will be power hogs
Power of 31 watts per port or much higher will be a requirement for 8x8:8 APs
Two PoE Plus cable runs will be needed or else the AP radio downgrades to a 4x4:4
POWER HOGS

## Slide 65
The main advantage of 8x8:8 AP is to take advantage of MU-MIMO capabilities which 802.11ax clients will need to support:
Less than 5% of the currently available clients support MU-MIMO
  Hardly any MU-MIMO capable clients exist in the current marketplace and the technology is rarely used in the enterprise
Which is better? 8x8:8 or 4x4:4 APs?

## Slide 66
Which is better? 8x8:8 or 4x4:4 APs?
Even if all clients supported MU-MIMO, the majority of modern-day enterprise deployments of Wi-Fi involve a high density of users that is not conducive for MU-MIMO conditions
  MU-MIMO requires spatial diversity, therefore physical distance between the clients is necessary
20 feet
25 feet
15feet
20 feet
30 feet

## Slide 67
Some of our competitors may manufacture an 8x8:8 access point using a Qualcomm IPQ8074 chipset. It will support eight 5 GHz streams and four 2.4 GHz streams. Some key points should be understood about 8x8:8 APs versus 4x4:4 802.11ax APs:
Marketing Fallacy #1: Vendor-X will claim that 8x8:8 AP will support more clients than 4x4:4 AP
Nonsense! - Regardless of stream count, all APs will support same number of Wi-Fi 6 capable clients
Which is better? 8x8:8 or 4x4:4 APs?

## Slide 68
Which is better? 8x8:8 or 4x4:4 APs?
Radio #1: SDR radio
Radio #2: Fixed 5 GHz Radio
2.4 GHz: Channel 6
5 GHz: Channel 40
5 GHz: Channel 100
The Power of Dual 5 GHz where Aerohive has been a leader!
Two dual-5 GHz 4x4:4 802.11ax radios transmitting on two separate 5 GHz (20 MHz) channels will provide better performance and efficiency.
Notes: There is no real advantage with an 8x8:8 AP over a 4x4:4 when using the OFDMA technology:
The competitor’s AP 8X8:8 radio will transmit on a single 5 GHz (20 MHz) channel and a single 2.4 GHz (20 MHz) channel.

## Slide 69
802.11ax WLAN design
802.11ax or any new Wi-Fi technology does not mitigate bad design
Design and validation are still key
Field testing will be vital

## Slide 70
802.11ax WLAN troubleshooting
802.11 management and control frames with 802.11ax information elements can be decoded
Already supported in Wi-Fi Explorer and the developer version of Wireshark

## Slide 71: 6 Ghz Wi-Fi Channels
U-NII-5: 5925-6425 MHz
U-NII-6: 6425-6525 MHz
U-NII-7: 6525-6875 MHz
U-NII-8: 6875-7125 MHz
Notes: 1.2 GHz more Wi-Fi (unlicensed) spectrum in the 6 GHz band. (UNII 5, 6, 7 & 8).
More than doubles the total amount of bandwidth available for Wi-Fi
But:
FCC
  Incumbent services in 6 GHz (Fixed satellite services, cable TV relay, Broadcast services, ( over 58k call signs…)
  Broadband will aim to use this band too.
  Multiple Power level restrictions
  Will need to protect existing and licensed services – whitespace (registry ?)and DFS like protection
EU – Only about half of the 6GHz band is available
IEEE - 11ax D3.2 already references support for 6 GHz band, need to add channel & power restrictions (IEEE).
Wi-Fi Alliance – Discussing adding support in 11ax certification, maybe part of Wave 2 -TBD
Broadcom – Wi-Fi Chipsets supporting 6 GHz in development
Clients - TBD
Aerohive – TBD
Other vendors – it's just marketing
Don’t expect anything to at least 2022

## Slide 72
Features:
Internal antennas
4x4 + 4x4 11ax
Dual band radio
1G + 1G ports
BLE / Zigbee / USB
POE+/DC Power
Features:
Internal antennas
4x4 + 4x4 11ax
Dual 5 GHz radio
2.5G + 1G ports
BLE / Zigbee / USB
POE+/DC Power
Redundant PoE capable
Features:
External antennas
4x4 + 4x4 11ax
Dual 5 GHz radio
2.5G + 1G ports
BLE / Zigbee / USB
Outdoor mode
Industrial Temp Range (-20C to +55C)
POE+/DC Power –
Redundant PoE Capable
AP630
AP650
AP650X
802.11ax – Next generation Wi-Fi has arrived!

## Slide 73: Twist and MOUNt

## Slide 74
TECHNICAL RESOURCES
802.11ax blog series: https://blog.aerohive.com/tag/11ax/
802.11ax for Dummies Booklet: https://content.aerohive.com/802.11ax_dummies_book

## Slide 75
Questions

## Slide 76: Thank you